## Slide 1: Smart VR Gloves Magic Mitts Final Design Review
Affordable Immersive VR Gloves
Team Members
Rabiat Sadiq, Blake Novosad,
John Navarro, Juan Casillas
Advisor
Ryan Saavedra

## Slide 2: John Navarro’s Contribution
Critical Redesign of PCBA
Critical power management redesign was brought to our attention 35 days before tech symposium
Unable to use boost converter enable lines, need to use more MOSFET switches
Added 4 key new components :
1 Isolated Boost Converter IC
2 Isolated Signal Integrity IC
5 More Mosfets
1 Resettable Fuse
Isolation IC
Isolated Boost IC
Final PCB Preview
MOSFET Switching

## Slide 3
Complete Detailed Schematic
PDF Schematic Links
High Level Schematic

## Slide 4: John Navarro’s Contribution
Curved Electromagnetic Housing Design
Designed with a smaller surface area on the users wrist/forearm (comfortable for more users)
Changed electromagnetic coil (EC) component
Old: Uxcell P25/20 EC (5V, 0.53A, 25mm Diameter)
New: Adafruit P25/20 EC (5V, 0.33A, 25.2mm Diameter)
Old Electromagnetic Design
New Electromagnetic Design
Increased spatial airflow between each individual electromagnetic coil
Extremely complex roof design that houses PCBA and routes more than 40 wires

## Slide 5: Juan Casillas Contribution
Bluetooth Connectivity
Attained bi-directional communication via BT communication
Initial BT communication through serial command while external power to ESP32
Button input transmitted through BT and output to serial monitor
Issues were mainly the use of correct COM port with proper BT initialization
Bluetooth factors to consider
BT latency when compared to serial connection
  Optimization for faster transmission over bluetooth
Proper BT pairing
  Maintain strong connection

## Slide 6: Blake Novosad’s Contribution
Combination Model
  combine battery pack with electromagnetic braking system
  need to add lids and housing for PCB
Current Combination STL

## Slide 7: Rabiat’s Contribution
Identifying Types of Grab
Implemented Oculus SDK HandGrabInteractable for precise grab recognition
Added real-time GUI display showing:
Current grab state
Active grabbing fingers
Grab type (pinch vs. full hand)
Object being grabbed
Recent Code Updates & System Integration
Grabbing detection
Identifying Types of Grab in VR space to send to Microcontroller
Notes: Testing Multiple Scenarios
Tested various object interactions and haptic feedback scenarios to ensure the system responds properly during real-world usage.

## Slide 8: Rabiat’s Contribution
System prepared for full 5-finger implementation:
5 flex sensor inputs (1600-3040 range)
5 haptic feedback channels
5 electromagnetic brake controls
Haptic feedback and electromagnetic system ready for hardware.
Code optimized for PCB integration
Although A challenge: Grab type detection sensitivity needs fine tuning, some inconsistency and requires full close
Interaction & Testing in VR
PCB Hardware Integration ready
Notes: Testing Multiple Scenarios
Tested various object interactions and haptic feedback scenarios to ensure the system responds properly during real-world usage.

## Slide 9: THANK YOU!
End of slides